## Slide 1
20231116

## Slide 2: This Week Progress
MEC has already connected to the Internet.
Survey about k8s DNS.

## Slide 3: This Week Progress
MEC has already connected to the Internet.
Survey about k8s DNS.

## Slide 4: Original Arch
UE/gNB
5G Core
Internet
GTP Processor
ONOS Controller
APPs
eno2
The flow MEC access to the Internet should go through the OVS.
Since host’s eno1 & eno2 have connected to the same AP, it will cause ARP storm.
 This way is a little bit troublesome
eno1
Notes: 麻煩點在於我要把eno2 attach到不同網段，所以我覺得會增加架設複雜度

## Slide 5: Current Arch
UE/gNB
5G Core
Internet
GTP Processor
ONOS Controller
APPs
UE accessing MEC
via the Multus path,
MEC accessing the Internet
via the Weave path.
Multus
Weave
eno1
Notes: APPs怎麼存取外網，具體來說APP透過weave分配的eth0(10.32.0.X)發送封包到10.32.0.1的本機上
本機就會收到封包，然後透過路由表將封包轉送到外網

## Slide 6: This Week Progress
MEC has already connected to the Internet.
Survey about k8s DNS.
  UE should access the pod via its domain name
  K8S has its own DNS server, so I survey it first

## Slide 7: About K8S local DNS server
User send DHCP packets
to the service
This service does
load balancing
SERVICE
POD

## Slide 8: About K8S local DNS server
Based on my research, the K8S DNS server can only translate domains name within the K8S internal network, for example
  When creating a Pod, a Pod domain name is established
    10-32-0-13.default.pod.cluster.local
  When creating a Service, a Service domain name is established
    svc-cluster.default.svc.cluster.local
The URLs resolved by the K8S DNS server belong to the above types rather than the conventional domain name, e.g., nginx.nems.com.

## Slide 9: About K8S local DNS server
A service type called ExternalName is another way to try.
Notes: ExternalName不是解決這個問題的方法。ExternalName是把外部應用包裝成service，讓內部pod存取該service就相當於存取該應用

## Slide 10: TODO List
Survey about Jake’s method.
Try to build the local DNS server