## Slide 1
20231228

## Slide 2: This Week Progress
Find the reason why the L4 protocol cannot be accessed.
Survey feasible ways.

## Slide 3: Problem Description
Encountered problem
L3 protocols can access APPs, but L4 protocols can not.
Check in deep
Packets between APPs and UE have wrong TCP checksum.

## Slide 4: Solution Survey
TCP offloading (better solution)
TCP checksum is randomly filled in OS, modified to correct one later by NIC.
Modify TCP checksum in ONOS
Let ONOS packetIn packets, and reset TCP checksum to 0.
Every receiver won’t check TCP checksum.

## Slide 5: TODO List
Fix the problem of TCP checksum.
FiberLogic’s TODO list
  Let ACL execute on ONOS.
  Move the system to Ubuntu 22.04.
  Redirect DNS request to 5G core if it miss MEC DNS record.
  Physical machines can attach to the OVS and act like MEC APPs.
  Let GTP processor learn other machines’ MAC automatically.
    May not needed, because they will abandon 5G arch in the future.

## Slide 6: Feedback
快速確認ubuntu 22.04的k8s運作，並交付
首先完成3,4