## Slide 1
20240222

## Slide 2: This Week Progress
Design HA architecture based on their proposed design.
QoS experiment is still in progress.
Notes: 架構有共識
QoS實驗有遇到問題

## Slide 3
Architecture

## Slide 4
Internet
Notes: 上次有問題的是紅、黑，然後我們討論之後覺得這個設計有問題。
VIP黏在HA port上，UE送ARP時，UE port收的封包其 MAC 不匹配。

## Slide 5: HA Architecture
UE 1
MEC
APPs
ACL
MEC
OVS-DPDK
APPs
UE 2
UE 3
MEC
APPs
ACL
ACL
QoS
QoS
Network
HA
Internet
Internet
L2 switch
OVS-DPDK
OVS-DPDK
SDN APP
QoS
Notes: 他們是開L2 switch需求，那QoS就只能做在OVS-DPDK。
如果QoS做在OVS，那麼上半年計劃的QoS實驗要繼續做嗎？

## Slide 6: APPs Architecture in K8S
Network
HA
Path for K8S APP Traffic
ACL
APP1
APP3
APP2
Host
192.168.0.7
Network
HA
OVS-DPDK
OVS can bind IP to a port,
and the host is accessible
by this IP.
QoS
Notes: 因為這次有多個節點，每個節點都會有 replica，所以不能像之前一樣讓 APP 直接連接到 OVS。
必須透過上面這個接法才能做到 load balance。

## Slide 7: APPs Architecture in K8S
Network
HA
Path for K8S APP Traffic
ACL
QoS
APP1
APP3
APP2
Host
192.168.0.7
Network
HA
OVS-DPDK

## Slide 8
QoS Experiment Progress

## Slide 9
UE/GNB
CN
OVS-DPDK
GTP Processor
6
5
7
2
1
Bind9
(APP2)
Nginx
(APP1)
ONOS Controller
DynamicACL
Component | Choice |  | 
GTP Processor |  | V | V
OVS-DPDK |  |  | V
Bandwidth (Mbps) | 860.40 | 903.16 | 909.33
UE  CN
UE  APP
Component | Choice | 
GTP Processor | V | V
OVS-DPDK | V | V
DynamicACL |  | V
Bandwidth (Mbps) | 19.34 | 0.053
Wrong L3 header cause bottleneck.
Notes: 因為GTP Processor會包錯的IP，所以SDN APP要再重新改header內容，這裡就是一個bottleneck。

## Slide 10: Feedback
發信問智通
  黑線的用意，確認後再動工。
  用L2 switch還是用SDN switch。
老師要求
  QoS還是希望用DPDK的程式功能
  希望還是讓APP接到OVS：想想host放到OVS前面，這種架構可不可行
QoS的部分
  先把DPDK程式L3 header修好